## Slide 1: CH9. Host Controller Interface and commands ch10. Logical Link and adaptation protocol(l2cap)
RTLAB
YuJin Park

## Slide 2: CH9. Host Controller Interface and commands

## Slide 3: Host Controller Interface and Commands
Standard method of communication between the upper and lower layers
LE reuses the specification of the HCI layer for BR/EDR and extends it.
HCI Packet Types(LE)
  HCI Command Packets
  HCI Event Packet(LE Meta Event = 0x3E)
  HCI ACL Data Packet
GATT Based Profiles
Generic Access Profile
Generic Attribute Profile(GATT)
Attribute Protocol(ATT)
Security Manager (SM)
Link Layer
Physical Layer
L2CAP
Host Controller Interface (HCI)
Upper Layer
Lower Layer
Event
Code
Parameter Total Length
Event Parameter
0
Event Parameter
1
Event Parameter
…
Event
Code
(0x3E)
Parameter Total Length
Sub Event Code
Sub Event Parameter
0
Event Parameter
…
Format of BR/EDR Event Packet Types
Format of LE Meta Event Packet Types

## Slide 4: HCI Commands and Events
LE Command : HCI_LE prefix.
HCI Commands and Events
  Device Setup
  Controller Flow control
  Host flow control
  Controller Information
  Remote Configuration
  Device Discovery
  Connection Setup
  Connection State
  Physical Links
  Link Information
  Authentication and Encryption
  Testing

## Slide 5: Device Setup & Flow control
Device Setup
  HCI_Reset : reset the controller(physical layer) and Link layer.
Controller Flow Control
  HCI_Read_Buffer_Size, HCI_LE_Read_Buffer_Size
  Number_Of_Completed_Packets_Event
Host Flow Control
  Host_Buffer_Size_Command
  Host_Number_Of_Completed_Packets_Command
  Data_Buffer_Overflow_Event
White_List
  HCI_LE_Read_White_List_Size
  HCI_LE_Clear_White_List
  HCI_LE_Add_Device_To_White_List
  HCI_LE_Remove_Deivce_From_White_List
Host
Controller
Initialize count of buffers to Number of buffers
If count > 0
Decrement count by number of packets sent to the controller
Increment count by number of packets reported as processed by the controller
Packets Transmitted on LE-U logical link
HCI LE Read Buffer Size
HCI Read Buffer Size
LE ACL Buffer Size, Number of LE Buffers
HCI ACL Data Packet
Number of Completed Packet Event
Separate Buffers
Shared Buffers

## Slide 6: Controller & Remote Information
Controller Information
  HCI_Read_Local_Version_Information
  HCI_Read_Local_Supported_Command
  HCI_Read_Support_Features_Command
  HCI_LE_Read_Support_Features_Command
  HCI_LE_Read_Supported_States
Remote Information
  HCI_LE_Read_Remote_Used_Features(Encryption Only)
  LE_Read_Remote_Used_Feature_Complete

## Slide 7: Controller configuration
Controller Configuration Commands
  HCI_LE_Set_Advertise_Enable
  HCI_LE_Set_Advertising_Data
  HCI_LE_Set_Advertising_Parameters
  HCI_LE_Set_Random_Address
  HCI_LE_Set_Scan_Response_Data
  HCI_Read_LE_Host_Support
  HCI_Write_LE_Host_Support

## Slide 8: Device Discovery and Connection
Device Discovery
  HCI_LE_Set_Scan_Enable
  HCI_LE_Set_Scan_Parameters
  HCI_LE_Advertising_Report_Event
Connection Setup
  HCI_LE_Create_Connection
  LE_Connection_Complete_Event
  HCI_Disconnet
  Disconnetion_Complete_Event
Connection State
  HCI_LE_Connection_Update
  LE_Connection_Update_Complete_Event

## Slide 9: Physical Link & Link Information
Physical Link
  HCI_LE_Set_Host_Chnnel_Classification(Channel map)
Link Information
  HCI_Read_Transmit_Power_Level
  HCI_Read_RSSI
  HCI_LE_Read_Advertising_Channel_Tx_Power
  HCI_LE_Read_Channel_Map

## Slide 10: Authentication and Encryption
HCI_LE_Encrypt
HCI_LE_Long_Term_Key_Requested_Event
HCI_LE_Long_Term_Key_Request_Reply
HCI_LE_Long_Term_Key_Request_Negative_Reply
HCI_LE_Rand
HCI_LE_start_Encryption
Ecryption_Change_Event
Encryption_Key_Refresh_Complete_Event

## Slide 11: Testing
HCI_LE_Receiver_Test
HCI_LE_Transmitter_Test
HCI_LE_Test_End

## Slide 12: Usage of White Lists
HCI_LE_Set_Advertising_Parameters
HCI_LE_Set_Scan_Parameters
HCI_LE_Create_Connction

## Slide 13: Practical Sequence Diagrams
Typical sequence for passive scanning
Host
Controller
Set Scan
Parameters
HCI_LE_Set_Scan_
Parameters
= passive scanning
ADV_IND
Host
Controller
Enable_Scanning
LE_Set_Scan_Enable
Link Layer State : Scanning
Set Advertising Parameters
HCI_LE_Set_Advertising_
Parameters
= Connectable_Undirected
Set Advertising Data
HCI_LE_Set_Advertising_
Data
Enable Advertising
HCI_LE_Set_Advertise_Enable = 1
LL State : Advertising
ADV_IND
Advertising Report
LE_Advertising_Report_Event
ADV_IND
Typical sequence for active scanning
Host
Controller
Set Scan
Parameters
HCI_LE_Set_Scan_
Parameters
= active scanning
ADV_IND
Host
Controller
Enable_Scanning
LE_Set_Scan_Enable
Link Layer State : Scanning
Set Advertising Parameters
HCI_LE_Set_Advertising_
Parameters
= Connectable_Undirected
Set Advertising Data
HCI_LE_Set_Advertising_
Data
Enable Advertising
HCI_LE_Set_Advertise_Enable = 1
LL State : Advertising
SCAN_REQ
Advertising Report
LE_Advertising_Report_Event
SCAN_RSP

## Slide 14: ch10. Logical Link and adaptation Protocol(l2cap)

## Slide 15: Logical Link control and Adaptation Protocol
Interface between the higher Layer protocols and the lower layers(Link/Physical Layer)
LE reuses the L2CAP functionality of BR/EDR
GATT Based Profiles
Generic Access Profile
Generic Attribute Profile(GATT)
Attribute Protocol(ATT)
Security Manager (SM)
Link Layer
Physical Layer
L2CAP
Host Controller Interface (HCI)
Upper Layer
Lower Layer

## Slide 16: PDU and SDU
Protocol Data Unit
Service Data Unit
Maximum Transmission Unit(MTU)
  Maximum size of SDU
  LE minimum MTU : 23 octets
Attribute Protocol
Attribute Protocol
L2CAP
L2CAP
SDU
SDU
L2CAP PDU
Maximum size depends on MTU

## Slide 17: Basic Assumptions
The Packet delivered in the correct sequence.
Only one LE-U logical link exists between the two devices.
The controllers provide a degree of reliability by including error detection, and retransmission mechanisms.
The controller provide flow control mechanisms for data going over the air as well as data going over the HCI transport layer

## Slide 18: L2CAP Features
Fixed Channel Identifiers
  Attribute Protocol (CID : 0x0004)
  LE L2CAP Signaling Channel (CID : 0x0005)
  Security Manager Protocol (CID : 0x0006)
Fragmentation and Deflagmentation of data
Multiplexing and Demultiplexing of various channels over a shared logical link(LE-U)

## Slide 19: Data Packets & L2CAP Parameters
MTU : 23 octets
Flush Timeout : 0xFFFF (Infinite)
Quality of Service : Best Effort
Mode : Basic mode
Length
(2 octets)
Channel ID
(2 octets)
Information Payload
LE L2CAP Data Packet Format

## Slide 20: L2CAP Signaling
Command Reject (code : 0x01)
Connection Parameter Update Request (code : 0x12)
  Interval Min
  Interval Max
  Slave Latency
  Timeout Multiplier
  (Connection Supervision Timeout = Timeout Multipler * 10 ms)
Connection Parameter Update Response (code : 0x13)

## Slide 21: HCI Connection Sequence

## Slide 22: HCI Connection Sequence

## Slide 23: HCI Connection Sequence

## Slide 24: L2CAP Connection Sequence(Classic)

## Slide 25: L2CAP Connection Sequence(Classic)

## Slide 26: L2CAP Connection Sequence(Classic)

## Slide 27: L2CAP Connection Sequence(Classic)

## Slide 28: L2CAP Connection Sequence(Classic)

## Slide 29
END.